## Slide 1
STM32 Ecosystem workshop
ST LATAM team

## Slide 2: Goal of this session
2
Get to know a little of ST’s 32-bit MCUs portfolio
To be able to create an application using STM32CubeMX
To be able to perform basic configuration, project processing and code writing within System Workbench For STM32 (SW4STM32) toolchain
To understand the concept of Hardware Abstraction Layer (HAL) and Low Layer (LL) libraries.
To be able to use some complementary debug tools
To be able to use the STM32 ODE pack libraries
To check the following applications examples: Bluetooth Low Energy/ MEMS / CLOUD BLUEMIX

## Slide 3: Microcontrollers ST has licensed all Cortex-M™ cores
Forget traditional 8/16/32-bit classifications and get
  Seamless architecture across all applications
  Every product optimized for ultra-low power and ease of use
www.st.com/stm32
MCU
Binary and tool compatible
Cortex-M0/M0+
Cortex-M3
Cortex-M4
16/32-bit applications
16/32-bit applications
16/32-bit DSC applications
Cortex-M7
16/32-bit DSC applications

## Slide 4: Microcontrollers Today – STM32 portfolio overview
STM32F2x5
STM32F2x7
Ultra-low-power
Mainstream
Cortex-M0
Cortex-M0+
Cortex-M3
Cortex-M4
Cortex-M7
STM32F030 Value line
STM32F0x1
STM32F0x2
STM32F0x8
STM32F301
STM32F302
STM32F303
STM32F3x4
STM32F373
STM32F3x8
STM32F100 Value line
STM32F101
STM32F102
STM32F103
STM32F105
/107
STM32F401
STM32F411
STM32F405/415
STM32F407/417
STM32F427/437
STM32F429/439
STM32L0x1
STM32L0x2
STM32L0x3
STM32L100 Value line
STM32L151/152
STM32L162
High-performance
STM32F746/756
6
1
2
STM32L4x1
STM32L4x2
STM32L4x3
STM32L4x5
STM32L4x6

## Slide 5: Workshop rules
3
For anyone that wants to redo this material, all the content and a lot of other usefull itens are available at my github page www.github.com/montanari9 The repository name is ARGENTINA, just download the USER_MATERIAL.zip file
All the exercises will be done by the trainer, but can be done by any participants with the tools.
In case of any trouble with the exercise it is possible to reuse from USER_MATERIAL:
  Existing ready STM32CubeMX project for particular exercise (_STM32CubeMX projects folder)
  Existing starting SW4STM32 project:
.\_SW4STM32 projects\STM32_Ecosystem_workshop_startups.zip
  Source files modifications needed for each exercise: (Sources folder)
Already completed SW4STM32 project
.\_SW4STM32 projects\STM32_Ecosystem_workshop_solutions.zip

## Slide 6: Training material overview
4
Folder name | File name | description
_STM32CubeMX projects | .ioc | Configured STM32CubeMX project files for each exercise
_Sources | sine.h | Sine buffer example for all F4_USART based exercises
 | template_src.c | Parts of the source code needed for each exercise.
_SW4STM32_projects | STM32_Ecosystem_workshop_startups.zip | Initial projects for each exercise.
 | STM32_Ecosystem_workshop_solutions.zip | Completed projects for each exercise
Documentation | *.pdf | Documentation referenced in the workshop (including board schematics)
Slides | *.pptx | Slides from the workshop

## Slide 7
Agenda

## Slide 8: Agenda
6
Creation and tuning of a simple project
System Workbench For STM32 (SW4STM32) toolchain
Complementary tools for debug (STMStudio and STLINK Utility)
Run the MEMS code 
Run the BLE Code with the MEMS and check the app!
Run the MEMS Cod e along with WIFI + MQTT to turn into a gateway application with IBM BlueMix and check the link!

## Slide 9
Glossary

## Slide 10
Explanation of the acronyms
ETM - Enhanced Trace Macrocell
ITM - Instrumentation Trace Macrocell
HAL Libraries – Hardware Abstraction Layer Libraries
LL Libraries – Low Layer Libraries
MSP/msp – microcontroller support package
PPP – marking of any peripheral – used to indicate name of the function, structure common for many peripherals
SVN – Subversion, Version Control System – one of the tool for sharing the software projects within working groups
SW4STM32 – System Workbench for STM32 – free toolchain for STM32 microcontrollers based on Eclipse
SWD - Single Wire Debug
SWIM – Single Wire Interface Module – programming/debugging interface in STM8 microcontrollers
SWO – Single Wire Output – one wire trace interface available in CortexM based microcontrollers (except CortexM0 and CortexM0+)
TRGO - Trigger Output - internal output signal of the timer used for synchronization with other peripherals (timers, DAC, ADC)
8

## Slide 11
Installation of the tools and drivers

## Slide 12: Checklist
Download, install SW4STM32 and upgrade it to the newest version
Download and install STM32CubeMX
Download and install STM32F4-Cube Libraries
Download and install STM32 STLink Utility
Download and install ST-Link V2.1 drivers
Download and install STMStudio
Download and install terminal application (i.e.Termite or HTerm)
10

## Slide 13
Installation of SW4STM32
System Workbench For STM32

## Slide 14
In order to download SW4STM32 toolchain you need to register on
www.openstm32.org website
After registration and logging, please either go to the web itself and:
  Select „System Workbench for STM32” from left side menu (it is called SW4STM32 as well).
  Select „Downloading the System Workbench for STM32” link from Table of Contents.
  Download and run
install_sw4stm32_win_64bits-latest.exe for 64-bit or
install_sw4stm32_win_32bits-latest.exe for 32-bit MS Windows.
In our session we will use “installation from MS Windows” option only.
12
Install SW4STM32 toolchain 1/2
installation from MS Windows

## Slide 15
Install SW4STM32 toolchain 2/2
installation from MS Windows
Launch System Workbench for STM32 installer.
You will receive pop-up error message displayed in case proper JavaRE version is not
installed on your system. Click "Ok" to get redirected to the Oracle JAVA website.
  Warning : The architecture version for System Workbench for STM32 MUST follow your Java architecture version. SW4STM32 64-bits will only work with JavaRE 7 (and newer) 64-bits etc.
The first page describes the product features. Get familiar, click “Next” to continue.
Read and accept the license agreement to continue installation. Click “Next” to continue.
Choose installation path (default: C:\Ac6\SystemWorkbench). Click “Next” to continue.
NOTE: Avoid paths with white spaces included like "C:\Program Files\...".
Follow the installation and, after “Finish” message is displayed, click “Quit” to exit installer.
13

## Slide 16
Update SW4STM32 to current version
configuration of automatic updates
In order to configure automatic finding new updates, please follow the procedure within SW4STM32:
Window -> Preferences
Install/Update –> Automatic Updates
Check “Automatically find new updates and notify me”
Configure Update schedule, download options and action to be done once updates are found accordingly
8

## Slide 17: Checkpoint #1 verification of SW4STM32 installation
9
Help->About Eclipse

## Slide 18
STM32CubeMX installation
Standalone version

## Slide 19: STM32Cube Install
STM32CubeMX tool
  http://www.st.com/stm32cube
The STM32CubeMX tool needs Java
  Please check whether you have latest Java installed on your PC, for sure 32-bit and 64-bit version
You can either download STM32CubeF4 packages directly from STM32CubeMX or download them offline using the below links and install as local (“From loc…” button)
  STM32CubeF4
12

## Slide 20: STM32Cube configuration 1/3
In case you download packages from web, you need to define place where they will be stored (repository)
MENU>Help>Updater Settings…
You will see current repository folder location
  Default is C:/User/Acc_name/STM32Cube/Repository/
  NOTE: In case your repository path contains diacritics, STM32CubeMX may fail to recognize them correctly. If this happens, change your repository path to contain raw Latin only (ex: C:/Repository)
You can either download STM32 packages manually and put them
into this folder or STM32CubeMX can do it for you if configured correctly
13

## Slide 21: STM32Cube configuration 2/3
The comparison of the STM32CubeMX repository settings and folder structure
In case you want STM32CubeMX to download these files automatically
  MENU>Help>Install New Libraries
  Select required libraries
  Force download with button “Install Now”
14
STM32CubeMX can download for you repository packages automatically

## Slide 22: STM32Cube configuration 3/3
The comparison of the STM32CubeMX repository settings and folder structure
In case you want to install files manually
  MENU>Help>Install New Libraries
Click “From Local…” button
Browse to select file to be installed
i.e. from provided USB stick package:
\HAL\STM32Cube_FW_F4_V1.13.0.zip
15

## Slide 23: STM32CubeMX install
For code generation STM32CubeMX uses package from the Repository folder
Currently, STM32CubeMX can generate code for the following toolchains
  Keil (free for F0/L0 families)
  IAR
  Atollic (free Lite version available)
  System Workbench (SW4STM32 by AC6, free)
For debugging purposes, it is necessary to have ST-Link drivers installed.
Drivers are a part of ST-Link Utility package that can be found here
  STSW-LINK004 ST-link Utility
To install drivers you will need Admin rights on your PC
16

## Slide 24: Checkpoint #2 verification of STM32CubeMX installation
17
Help->About
Help->Install New Libraries

## Slide 25
Installation of STM32 ST-Link Utility

## Slide 26: Download & Install STM32 ST-Link Utility
Drivers are available for Windows XP, Vista, 7, 8 & 10.
To download them use direct link:
http://www.st.com/content/st_com/en/products/embedded-software/development-tool-software/stsw-link004.html
Unzip the package and run executable (setup.exe)
Follow all default installation settings
23

## Slide 27
Installation of ST-Link v2.1 drivers

## Slide 28
Download & Install ST-Link/V2-1 drivers
Drivers are available for Windows XP, Vista, 7, 8 & 10.
To download them use direct link:
  http://www.st.com/content/st_com/en/products/embedded-software/development-tool-software/stsw-link009.html
Unzip the package and run executable for x86 or AMD micro, depending on the platform you use
Follow all default installation settings
25

## Slide 29
Installation of STMStudio application

## Slide 30: Installing STMStudio
Ensure that the Java Run Time Environment (JRE) is installed and running on your machine.
JRE version 1.7 or more recent is required (JRE 7).
If installed JRE version is older than 1.7 or you miss it, please download the latest one from:
http://www.oracle.com/technetwork/java/javase/downloads/index.html.
Note that STM-STUDIO requires 32-bit JRE installed (even on 64-bit versions of Windows).
STMStudio can be found on www.st.com by putting stmstudio keyword into the search field
Once the JRE is installed or updated, run STMStudio_setup.exe.
27

## Slide 31
Now it is a right time for some slides
We will present briefly what is STM32CubeMX and the structure of the Cube library
2

## Slide 32
What it is STM32CubeMX ?

## Slide 33: STM32CubeMX application
STM32CubeMx do allow to configure peripherals using GUI, generate project framework and peripheral initialization code.
STM32CubeMx do not allow to create algorithms using GUI and generate algorithms code yet – there is still some space for programmers left ;-)
5

## Slide 34: What it is STM32CubeMX ?
6
Pinout Wizard
Clock Tree Wizard
Peripherals & Middleware Wizard
Power Consumption Wizard
STM32CubeMX
Generates Initialization C Code based on user choices !

## Slide 35: STM32Cube FW Package Organization
Supporting files like fonts, pictures for graphic examples, …
7
Can be found in STM32CubeMX repository
STM32xxCube HAL package
Documents
Drivers
Middleware
Projects
Utilities
Getting started with STM32F4Cube document

## Slide 36: STM32Cube FW Package Drivers
Drivers
CMSIS
STM32Fxxx_HAL_Driver
BSP
8
Register definitions for Core, startup files, ARM cortex libraries
Cube F4 HAL package
Documents
Drivers
Middleware
Projects
Utilities
HAL drivers for each periphery in STM32
Functions using HAL drivers to communicate with other components present on EVAL/Discovery boards

## Slide 37: STM32Cube FW Package Middleware
9
Middleware
ST
STemWin
STM32_Audio
STM32_USB_Device_Library
STM32_USB_Host_Library
Third Party
FatFS
FreeRTOS
LibJPEG
LwIP
PolarSSL
Advanced set of libraries
Third Party libraries
Developed/Owned by ST
Cube F4 HAL package
Documents
Drivers
Middleware
Projects
Utilities

## Slide 38
10
Projects
STM32F-Discovery
Templates
Examples
Applications
Demonstrations
….
Complete projects for STM32 boards
STM32Nucleo, Discovery kits, Eval Boards
Empty project only with startup file prepared for modification
Demonstration project combining multiple Middleware together
Cube F4 HAL package
Documents
Drivers
Middleware
Projects
Utilities
Advanced examples using Middleware (USB virtual com port)
Simple examples for STM32 Peripheries (GPIO, USART, …)
STM32Cube FW Package Projects

## Slide 39
Preparation of the hardware

## Slide 40: What we would need ?
Mini-USB cable
PC with preinstalled software (STM32CubeMX, SW4STM32, STLinkv2.1 drivers)
NUCLEO-F401RE board
12
Reset
User Button on PC13
LD2 on PA5
STLink v2.1

## Slide 41
Now it is a right time for some software activity
Our first task is to create LED blinking application – just to check whether all the software packs and drivers are installed correctly and whether the hardware is ready for more challenging job
13

## Slide 42
To practice a little bit with STM32CubeMX by:
MCU selection
Play a bit with clock configuration for STM32F4 device
Create a skeleton of simple LED blinking application
Have some fun!
14
Goal of this part

## Slide 43
Creating the ‘F4_Blinky’ example in STM32CubeMX

## Slide 44
Creating a New Project
1. From the STM32Cube Home Page or Menu  File
select New Project
2. There are 3 ways to create a New Project
By STM32 Series and Product Line
By Peripheral Mix
By Board
3. For this example we will use NUCLEO–F401RE
Select the Board Selector Tab from the top left
Select Type of Board to be Nucleo64
Select STM32L4 in MCU Series
Select the NUCLEO–F401RE from the list on the right
Click ‘OK’ to continue
16
1
2

## Slide 45: Peripheral and Pin Configuration
You will be presented with the pinout of the NUCLEO–F401R#
The debug pins, Push Button and LED are already highlighted in green, to say they are connected to the hardware on the board.
System Pins are highlighted in yellow/yellow-grey
Optional Hardware, like crystals and USART are highlighted in orange. This means there are PCB connections but not necessarily any hardware connected by default.
For the “F4_Blinky” example all relevant peripherals are
already connected, so no modifications are needed.
17

## Slide 46: Clock Configuration
1. Select ‘Clock Configuration’ tab
Select HSI in PLL Source Mux (HSI – High Speed Internal clock)
Select PLLCLK in the System Clock Mux
Set HCLK to 84 and press ENTER – application will propose PLL configuration to match this
requirement
18
Task: Configure clock system to use internal oscillator with PLL @84MHz
1
2
3
4

## Slide 47: Peripheral Configuration
Select ‘Configuration’ tab
In this section peripherals with no physical pins or middleware can be added to the project
For the ‘F4_Blinky’ example no additional configuration is required as LED is already
configured in GPIO link as Output Push-Pull.
19

## Slide 48: Configure the code generator 1/2
Open project setings:
  Menu  Project  Settings
Under Project tab:
  Give the project a name and location (i.e. F4_Blinky)
  We strongly recommend to place this folder on the root of ‘C:’ as some C-compilers show issues when the build path contains too many characters
  Select the toolchain to be SW4STM32
For better understanding let’s review code generation options (Code Generation tab) first
20

## Slide 49: Configure the code generator 2/2
21
Code generator options
  Copy either the full library or only the necessary files or just link the files from the common repository
  Place all peripherals initialization in the stm32fxx_hal_msp.c file or one file per peripheral
  Keep user code or overwrite it (refers to code placed between user code comment sections)
  Delete or keep files that are not used anymore
  Set unused pins as analog to keep consumption low (if SWD/JTAG is not selected in pinout, this option will disable it)
  Enable full assert in project, this helps to discover incorrect HAL function parameter used in user code

## Slide 50: Code generation
Once we have configured the code generator, we can generate code for selected toolchain.
There are 3 ways to do it, namely:
  Clicking icon
  Pressing Ctrl+Shift+G keys combination
  Selecting ProjectGenerate Code option from menu
When prompted, click ‘Close’ (we will import this project from SW4STM32 IDE).
22

## Slide 51
After successful code generation by STM32CubeMX this is the right time to import it into SW4STM32 toolchain for further processing
2

## Slide 52
Handling the project in SW4STM32

## Slide 53: Our goals for this session
Handling the projects generated by STM32CubeMX in SW4STM32
Import project generated by STM32CubeMX
Tune sources to run selected peripherals in desired algorithm
Build project
Configure debug session
Run debug session
Debug perspective
Watching the variables and registers content
Handling errors
5

## Slide 54: Create a new workspace - SW4STM32
Start Workspace launcher if not done automatically by Eclipse.
6

## Slide 55: Create a new workspace
Create new workspace in the desired location – but not in the same folder where
the project which will be imported is located (it must be one level above the project)
7
An empty workspace will be generated

## Slide 56: Import the project into the workspace 1/3
IMPORT project into workspace
Import “F4_Blinky” project into empty workspace following below steps:
8
This is possible to import multiple projects into a single workspace

## Slide 57: Import the project into the workspace 2/3
9
In this example F4_Blinky project will be processed.
1
3
Select project location
(as configured in STM32CubeMX –
Step2)
2
4

## Slide 58: Import the project into the workspace 3/3
10
Once project is included into the workspace, its folder structure becomes visible in Project Explorer
Places dedicated for user code are marked by
/* USER CODE … BEGIN*/
and
/* USER CODE … END*/
comment lines.
These places are protected from being removed during code re-generation by STM32CubeMX.
This is possible to define another user code places in .c
source files but not possible in .h header files.
Warnings and errors after build the project

## Slide 59
STM32CubeMX generated project is only a skeleton which should be filled with some code from our side
To make green LED (connected to properly configured PA5 pin) we should continuously invoke GPIO toggle function with the proper delay to make blink visible
11

## Slide 60: Modifying the code – Blink LED
12
Tasks (within while(1) loop in main.c):
Add GPIO pin toggle function for PA5 pin. Which function we can use here?
?
Add 500ms delay between each change of the GPIO pin state. Which function we can use here?
?
Hints:
All HAL function begins with HAL_PPP_ prefix (PPP – short name of the peripheral, i.e. GPIO)
Please try to use Content Assistant (Ctrl+SPACE) in Eclipse

## Slide 61: Modifying the code – Blink LED
13
Solutions (within while(1) loop in main.c):
Add GPIO pin toggle function for PA5 pin. Which function we can use here?
HAL_GPIO_TogglePin();
Add 500ms delay between each change of the GPIO pin state. Which function we can use here?
HAL_Delay();
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE
END WHILE */
/* USER CODE BEGIN 3 */ HAL_GPIO_TogglePin(GPIOA, GPIO_PIN_5);
HAL_Delay(500);
}
/* USER CODE END 3 */

## Slide 62: Useful project settings in SW4STM32
14
configuring C dialect and parallel build
1. Configure C standard to C99 to avoid possible compilation errors
1
2. Check Enable parallel build to make use of your machine potential and to shorten compilation time
Project->Properties
C/C++ Build->Settings->Tools Settings tab->MCU GCC Compiler->Dialect
C/C++ Build->Behavior tab
2

## Slide 63: Compiler optimization levels
8
Optimization levels are accessible within project properties (right click the project name)
Within project Properties select:
C/C++ Build -> Settings ->Tool Settings->MCU GCC Compiler->Optimization From
From drop-down menu select required optimization level
Click Apply->OK buttons when completed

## Slide 64: Issue with missing _IRQn
During code generation with “Generate
Under Root” option selected, all header files for a complete family are added to the project causing an error with unresolved parameter (too many sources with the same definition)  this is necessary to change indexer settings.
9
uncheck this option
check this option
Project Properties->C/C++ General->Indexer

## Slide 65: Building the project in SW4STM32
15
To build the project press Ctrl+B or click Make All icon
In case of multiple compilation
errors, re-run Indexing of the project
After proper build there are information about code/data space usage in Console window displayed

## Slide 66: Configure the debug session in SW4STM32
16
for single project in the workspace
Before running debug session this is necessary to configure it for current project
In case there is a single project in the workspace this is enough to click the “bug” icon and:
Select “Ac6 STM32 C/C++ Application”
line and click ‘OK’
In case the project was generated on existing/defined board (like NUCLEO- LF401RE in our example) debug will run automatically
Next step would be to run the debug session
(see the next slide)
1

## Slide 67: Configure the debug session in SW4STM32 for multiple projects in the workspace
17
Before debugging current project for the first time, this is necessary to configure its debug session
Double click (or use right mouse button
to select) to create a new debug configuration for the current project
All project parameters should
be filled-in automatically
Select Debug Configuration
option
1
2
3

## Slide 68: Debug session perspective watching the variables
20
This is possible to monitor CPU registers, peripherals registers and variables during debug session, but we need to pause the code execution (no live view is possible for the time being).
To add variable to be monitored - highlight it, press right mouse button and select “Add Watch Expression”. It will appear in Expressions tab then.
Values which has changed from previous project pause will be presented on yellow background
Watched variables
Values changed from previous application pause

## Slide 69: Debug session perspective watching the registers content
21
This is possible to monitor CPU registers, peripherals registers and variables during debug session, but we need to pause the code execution (no live view is possible for the time being).
To add peripheral register to watch - click right mouse button and select “Activate”. Peripheral icon and its registers names will be highlighted in green and will contain “caught” values on next debug pause.
Values which has changed from previous project pause will be highlighted in red.
Peripherals
Core registers
registers
Non-watched peripheral
Watched peripheral
Value changed from previous application pause

## Slide 70: Handling the debug session SW4STM32
22
Skip all breakpoints
Run/resume
Suspend
Terminate debug session
Disconnect from the target
Step into
Step Over
Step Return
1 2
3
4
5
6
7
windows configuration in debug perspective

## Slide 71: How would I do that with another toolchain and kit???

## Slide 72: STM32F072 Discovery
Gyroscope
Integrated ST-Link/V2-1 (for programming and debugging)
2 push buttons
4 LEDs
Touch Sense Slider

## Slide 73: STM32F072 Discovery
USB Device Connector
NFC / ACP connector
Direct access to all MCU I/Os

## Slide 74: Configure GPIO for LED toggling
Create project in CubeMX
  Menu > File > New Project
  Select Board> Discovery > F0 > STM32F072-DISCO
Notice the GPIO pins assigned to the LEDs

## Slide 75: Configure GPIO for LED toggling
Here we can re-use the same code, just changing the GPIO 
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE
END WHILE */
/* USER CODE BEGIN 3 */ HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_6);
HAL_Delay(200);
HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_7);
HAL_Delay(200);
HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_8);
HAL_Delay(200);
HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_9);
HAL_Delay(200);
}
/* USER CODE END 3 */

## Slide 76
Before adding a new code let’s go with some theory explaining the
Cube Library structure and what is generated by STM32CubeMX
Please don’t be mad at me, this will be quick ;)
2

## Slide 77: Goal of this part
Understand the structure of the code generated by STM32CubeMX
Know the role of the library files
Know the role of the functions executed before main
Understand interrupt handling process
4

## Slide 78
STM32CubeMX generated code

## Slide 79: STM32CubeMX generated codecode structure, main operations after the reset
6
It performs the following operations:
Enables Floating Point Unit (FPU) inside the core
Resets the Clock Configuration to the default reset state
Disables all Interrupts
Configures Vector Table location and its offset
It does NOT configure the clock system (as it was done in Standard Peripherals Library (SPL))
Located in: system_stm32f4xx.c
Called from: startup_stm32f4xx.s (reset vector before main())
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
HAL_PPP_Action(); while(1);
}

## Slide 80: STM32CubeMX generated code code structure, main operations after the reset
7
It performs the following operations:
Configures FLASH accelerator
Configures NVIC priority (group and sub-priorities split)
Configures SysTick for 1ms tick (based on HSI clock)
Initializes Low-level hardware selected in STM32CubeMX (call to HAL_MspInit() function)
Located in: stm32f4xx_hal.c
Called from: main.c
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
HAL_PPP_Action(); while(1);
}

## Slide 81: STM32CubeMX generated code code structure, main operations after the reset
8
It performs the following operations:
Configures Interrupts Priorities
(for each peripheral selected in STM32CubeMX)
Located in: stm32f4xx_hal_msp.c
Called from: stm32f4xx_hal.c
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
HAL_PPP_Action(); while(1);
}

## Slide 82: STM32CubeMX generated code code structure, main operations after the reset
9
It performs the following operations:
Configures System & Buses clocks
(based on STM32CubeMX clock settings)
Located in: main.c
Called from: main.c
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
HAL_PPP_Action(); while(1);
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User

## Slide 83: STM32CubeMX generated code code structure, main operations after the reset
10
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
It performs the following operations:
Initializes PPP peripheral based on STM32CubeMX configuration
Uses structures and dedicated initialization functions type HAL_PPP_Init()
Within those functions this is possible to tune a peripheral configuration
Located in: main.c
Called from: main.c
HAL_PPP_Action(); while(1);
}

## Slide 84: STM32CubeMX generated code code structure, main operations after the reset
11
It performs the following operations:
Initializes the PPP peripherial mode (according to parameters specified in the PPP_InitTypeDef structure) and the associated handler
Located in: stm32f4xx_hal_PPP.c
Called from: main.c
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
HAL_PPP_Action(); while(1);
}

## Slide 85: STM32CubeMX generated code code structure, main operations after the reset
12
It performs the following operations:
Configures Clocks related to PPP peripheral
Configures GPIO lines assigned to PPP peripheral
Configures DMA channel assigned to PPP peripheral (except source and destination address and number of the data to be transferred – this is done by HAL_PPP_Action() function)
Configures Interrupts selected for PPP peripheral
Located in: stm32f4xx_hal_msp.c
Called from: stm32f4xx_hal_PPP.c
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
STM32CubeMX
User
HAL_PPP_Action(); while(1);
}

## Slide 86: STM32CubeMX generated code peripherals initialization (DAC example)
13
All HAL_DAC_Init() functions
are calling the same function
HAL_DAC_MspInit()
Handler instance parameter
is used to determine which
DAC needs to be initialized
Initialize GPIO lines
selected in
STM32CubeMX
void HAL_DAC_MspInit(DAC_HandleTypeDef* hdac)
{
GPIO_InitTypeDef GPIO_InitStruct;
if(hdac->Instance==DAC)
{
/* USER CODE BEGIN DAC_MspInit 0 */
/* USER CODE END DAC_MspInit 0 */
/* Peripheral clock enable */
HAL_RCC_DAC_CLK_ENABLE();
/**DAC GPIO Configuration PA4 ------> DAC_OUT1
*/
GPIO_InitStruct.Pin = GPIO_PIN_4; GPIO_InitStruct.Mode = GPIO_MODE_ANALOG; GPIO_InitStruct.Pull = GPIO_NOPULL; HAL_GPIO_Init(GPIOA, &GPIO_InitStruct);
/* Peripheral DMA init*/
hdma_dac_ch1.Instance = DMA1_Channel2; hdma_dac_ch1.Init.Request = DMA_REQUEST_9; hdma_dac_ch1.Init.Direction = DMA_MEMORY_TO_PERIPH; hdma_dac_ch1.Init.PeriphInc = DMA_PINC_DISABLE; hdma_dac_ch1.Init.MemInc = DMA_MINC_ENABLE;
hdma_dac_ch1.Init.PeriphDataAlignment = DMA_PDATAALIGN_HALFWORD; hdma_dac_ch1.Init.MemDataAlignment = DMA_MDATAALIGN_HALFWORD; hdma_dac_ch1.Init.Mode = DMA_CIRCULAR;
hdma_dac_ch1.Init.Priority = DMA_PRIORITY_LOW;
if (HAL_DMA_Init(&hdma_dac_ch1) != HAL_OK)
{
Error_Handler();
}
HAL_LINKDMA(hdac,DMA_Handle1,hdma_dac_ch1);
/* USER CODE BEGIN DAC_MspInit 1 */
/* USER CODE END DAC_MspInit 1 */
}
}
Initialize DMA channel
selected in
STM32CubeMX
HAL_DAC_Init() function details
HAL_DAC_Init() start
HAL_DAC_MspInit() start
HAL_DAC_Init() end
Store Init structure into DAC registers
GPIO and linked DMA initialization
HAL_DAC_MspInit() end

## Slide 87: STM32CubeMX generated code code structure, main operations after the reset
14
It performs the following operations:
PPP peripherals control (i.e. Start, Stop, Calibration)
DMA configuration if needed (buffer location, source and destination addresses, number of data to be transferred)
Located in: main.c
Called from: main.c
STM32CubeMX
User
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
HAL_PPP_Action(); while(1);
}

## Slide 88: STM32CubeMX generated code - summary
15
Operation Function Origin
called from
source location
Enable Floating Point Unit (FPU) inside the core
Reset the clock configuration to the default reset state
Disable all interrupts
Configure vector table location and its offset
SystemInit()
startup_stm32xxxx.s
system_stm32xxxx.c
STM32CubeMX
Configure FLASH accelerator
Configure NVIC priority (group and sub-priorities split)
Configure SysTick for 1ms tick (based on HSI clock)
Initialization of low level hardware selected in STM32CubeMX (HAL_MspInit() function)
HAL_Init()
main.c
stm32xxxx_hal.c
STM32CubeMX
Configure Interrupts priorities (for each peripheral selected in STM32CubeMX)
HAL_MspInit()
stm32xxxx_hal_msp.c
stm32xxxx_hal_msp.c
STM32CubeMX
Configure System & Buses clocks based on STM32CubeMX clock settings
SystemClockConfig()
main.c
main.c
STM32CubeMX
Initialize PPP peripheral based on STM32CubeMX configuration:.PPP related peripheral configuration (GPIO lines, DMA channel) in function HAL_PPP_MspInit()
MX_PPP_Init()
main.c
main.c or PPP.c
STM32CubeMX
Connect Clock to the peripheral
Configure GPIO lines
Configure DMA channels (based on STM32CubeMX settings)
HAL_PPP_MspInit()
stm32xxxx_hal_msp.c
stm32xxxx_hal_msp.c
STM32CubeMX
Activate PPP peripherals control (i.e. Start, Stop, Calibration),
Configure DMA if needed (buffer location, source and destination addresses, number of data to be transferred)
HAL_PPP_Action()
main.c
user_code.c
User
SystemInit(); main()
{
HAL_Init()
{
HAL_MspInit();
}
SystemClockConfig();
MX_PPP_Init()
{
HAL_PPP_Init()
{
HAL_PPP_MspInit();
}
}
HAL_PPP_Action(); while(1);
}

## Slide 89: STM32CubeMX generated code code structure - interrupts
16
PPP_IRQHandler()
{
HAL_PPP_Callback();
}
operation | Function called from source location | Origin
Check all possible flags and interrupt triggers Clear all interrupts flags Call proper callback functions assigned to the particular interrupt source/trigger | PPP_IRQHandler() stm32xxxx_it.c stm32xxxx_hal_ppp.c | STM32CubeMX
Perform an action related to the specific interrupt. | HAL_PPP_Callback() user_code.c user_code.c | User

## Slide 90: So...how does the interrupt works with Cube?

## Slide 91: Configure EXTI which turns on LED
Objective
  Learn how to setup input pin with EXTI in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure GPIO and EXTI pin in CubeMX and Generate Code
  Add into project Callback function and function which turn on led
  Verify the correct functionality by pressing button which turns on LED

## Slide 92: Configure EXTI which turns on LED
Create project in CubeMX
  Menu > File > New Project
  Select Board> Discovery > F0 > STM32F072-DISCO
Keep the GPIO pins for the LED
Configure Button pin as GPIO_EXTIX

## Slide 93: Configure EXTI which turns on LED
GPIO Configuration
  TAB>Configuration>System>GPIO

## Slide 94: Configure EXTI which turns on LED
NVIC Configuration
  We need to enable interrupts for EXTI
  TAB>Configuration>System>NVIC

## Slide 95: Configure EXTI which turns on LED
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code

## Slide 96: Configure EXTI which turns on LED
HAL Library work flow 1
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
Generated by CubeMX

## Slide 97: Configure EXTI which turns on LED
HAL Library work flow 2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
MX_GPIO_Init
inside main.c

## Slide 98: Configure EXTI which turns on LED
HAL Library working flow 3
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
inside stm32f4xx_it.c

## Slide 99: Configure EXTI which turns on LED
HAL Library work flow 4
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
User must define Callback it is declared by default as empty weak

## Slide 100: Configure EXTI which turns on LED
HAL Library work flow 5
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
Usually in main.c between /* USER CODE BEGIN */
tags

## Slide 101: Configure EXTI which turns on LED
HAL Library work flow summary
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
2. init GPIO
1. init NVIC
3. create edge
4. EXTI interrupt handler
5. HAL EXTI interrupt handler
6. HAL EXTI callback
HAL files clearing flags, check errors, …

## Slide 102: Configure EXTI which turns on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on we need to use this functions
  HAL_GPIO_WritePin

## Slide 103: Configure EXTI which turns on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on/off we need to use this functions
void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin){
if(GPIO_PIN_0==GPIO_Pin) {
HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_6);
}
}

## Slide 104
HAL libraries
basic information

## Slide 105: HAL library function naming convention
18
HAL_StatusTypeDef HAL_PPP(Ex)_Operation_mode()
Return value:
HAL_OK
HAL_ERROR
HAL_BUSY
HAL_TIMEOUT
void for simple peripherals (i.e. GPIO)
HAL prefix indicating type of the library (in contrary to Low Layer (LL)
PPP – periperheral name. If ‘Ex’ suffix is added it means that this particular function is related to current MCU family line and cannot be directly migrated to other STM32 lines
Type of the operation on the peripheral, like ‘Start’, ‘Stop’
Mode of the operation:
polling – no suffix
Interrupt – suffix IT
DMA – suffix DMA
See next slides for further details
Hint: to find proper function for the peripheral, please type HAL_PPP_ and press Ctrl+Space

## Slide 106: HAL library actions on peripherals
19
Most of the configuration procedures are prepared and generated by
STM32CubeMX based on user configuration
After this process, within main() function, user should prepare series of the
functions which would activate the selected peripherals in required mode:
  Polling mode (function type HAL_PPP_Action() )
  Interrupt mode (function type HAL_PPP_Action_IT() )
  DMA mode (function type HAL_PPP_Action_DMA() )
Hint: to find proper function for the peripheral, please type HAL_PPP_ and press Ctrl+Space

## Slide 107: HAL library actions on peripherals – polling mode
20
The HAL functions return the process status when the data processing in blocking mode is complete. The operation is considered to be completed when the function returns the HAL_OK status, otherwise an error status is returned. The user can get more information through the HAL_PPP_GetState() function.
The data processing is handled internally in a loop.
A timeout (expressed in ms) is used to prevent process hanging.
Examples:
Hint: to find proper function for the peripheral, please type HAL_PPP_ and press Ctrl+Space
HAL_UART_Transmit(&huart1, buffer_tx, 10, | 100 | );
HAL_SPI_TransmitReceive(&hspi1, buffer_tx, buffer_rx, 10,100); |  | 

## Slide 108: Peripheral HAL driver model Blocking polling process
Blocking polling process APIs
  Block until end of the process, or exit with timeout , error or busy
  Ex: HAL_USART_Receive()
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
(ex: HAL_USART_Receive)
HAL_BUSY
Non blocking start process
  Exits directly after starting the process
  Used mainly for ADC,DAC, Timer
  Ex: HAL_ADC_Start()
Peripheral Initializations
Start Process
(ex: HAL_ADC_Start)
Poll for process complete
(ex: HAL_ADC_PollForConversion)

## Slide 109: HAL library actions on peripherals – interrupt mode
21
The HAL function returns the process status after starting the data processing and enabling the appropriate interrupts.
The end of the operation is indicated by a callback declared as a function with a weak attribute. It can be safely customized (overwritten) by the user in the USER CODE section then.
In interrupt mode, four functions are declared in the driver:
HAL_PPP_Process_IT();
HAL_PPP_IRQHandler();
•
•
launch the process
the global PPP peripheral interrupt
weak HAL_PPP_ProcessCpltCallback (); the callback related to the process completion.
weak HAL_PPP_ProcessErrorCallback(); the callback related to the process Error.
To use a process in interrupt mode, HAL_PPP_Process_IT()
HAL_PPP_IRQHandler in stm32l4xx_it.c.
Examples:
is called in the user file and
HAL_UART_Transmit_IT (&huart1, buffer_tx, 10);
HAL_SPI_TransmitReceive_IT (&hspi1, buffer_tx, buffer_rx, 10);

## Slide 110: Peripheral HAL driver model Non Blocking process with interrupt generation
Start process with interrupt generation at end of process
Ex: HAL_USART_Receive_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_PPP_IRQHandler
end of process callback
Ex: HAL_USART_RxCpltCallback
process Error callback
Ex: HAL_USART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY

## Slide 111: HAL library
22
actions on peripherals – DMA mode
The HAL function returns the process status after starting the data processing through the DMA and after enabling the appropriate DMA interrupt.
The end of the operation is indicated by a callback declared as a function with a weak attribute. It can be safely customized (overwritten) by the user in the USER CODE section then.
For the DMA mode, three functions are declared in the driver:
HAL_PPP_Process_DMA();
HAL_PPP_DMA_IRQHandler();
•
•
launch the process
the DMA interrupt used by the PPP peripheral
weak HAL_PPP_ProcessCpltCallback();the callback related to the process completion.
weak HAL_PPP_ErrorCpltCallback(); the callback related to the process Error.
To use a process in DMA mode, HAL_PPP_Process_DMA() is called in the user file and the HAL_PPP_DMA_IRQHandler() is placed in the stm32l4xx_it.c. When DMA mode is used, the DMA initialization is done in the HAL_PPP_MspInit() callback. The user should also associate the DMA handle to the PPP handle.
Examples:
  HAL_ADC_Start_DMA(&adc_handler, buffer_for_DMA, buffer_size);
  HAL_TIM_PWM_Start_DMA(&timer_handler, timer_out_channel, buffer_for_DMA, buffer_size);

## Slide 112: Peripheral HAL driver model Non blocking process with DMA transfer
Start process with DMA end of transfer interrupt generation at end of process
Ex: HAL_USART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
Ex: HAL_DMA_CpltCallback
DMA_Strream_IRQHandler
process Error callback
Ex: HAL_USART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR

## Slide 113: HAL library
23
DAC handler structure
DAC_HandleTypeDef
Instance
Status/error/locks
Parents/Links
Internal status information
DAC1
Ready Busy
Error
or
or
…
Linked to DMA for channel 1
ErrorCode
or
PPP_HandleTypeDef *handle is the main structure that is implemented in the HAL drivers. It handles the peripheral/module configuration and registers and embeds all the structures and variables needed to follow the peripheral device flow. It is used for the following purposes:
Linked to DMA for channel 2
Multi instance support: each peripheral/module instance has its own handle. As a result instance
resources are independent.
Peripheral process intercommunication: the handle is used to manage shared between the process routines. Example: global pointers, DMA handles, state machine.
Storage : this handle is used also to manage global variables within a given HAL driver.
data resources
An example for DAC peripheral
handler structures

## Slide 114: HAL library
24
DAC channel configuration structure
DAC_ChannelTypeDef
SampleAndHold
Trigger source
Output buffer
Interconnection
Sample and Hold configuration
External trigger selection
Enable/disable of the output buffer
Connection of DAC output to internal peripherals
These structures are defined in the generic driver header file when it is common to all part numbers. When they can change from one part number to another, the structures are defined in the extension header file for each part number.
User trimming
DAC trimming configuration
Trimming value
Examples for DAC peripheral:
DAC_ChannelConfTypeDef
DAC_SampleAndHoldConfTypeDef
DAC sample and hold structure
DAC_SampleAndHoldConf
Sample time
Hold time
Refresh time
Sample time for selected channel
Hold time for selected channel
Refresh time for selected channel
initialization and configuration of structures

## Slide 115
In our next task we will use a PC applications to monitor data sent by Nucleo board over STLink v2.1:
asynchronously using USART2 interface -> monitor on any terminal application
synchronously, using SWO interface -> monitor on STLink Utility application
3

## Slide 116
Complementary debug tools
Using printf() over SWO and USART2 to send data via USB to PC

## Slide 117
Using SWO
introduction
On most of STM32 (except STM32F0, L0 devices) there is peripheral called Instrumentation Trace Macrocell (ITM) (do not mix with Enhanced Trace Macrocell - ETM) available
This peripheral can be used to send-out data from MCU
over Single Wire Output (SWO) pin
It is possible to redirect printf() to use this peripheral
Most IDEs can display this information during debug
On 64pins Nucleo boards (NUCLEO_F401RE as well) SWO pin (PB3) is connected to the STLink (SB15 solder bridge is closed) so no additional connection is required to reuse this line
5

## Slide 118: Concept of the system sending measured data over SWO and USART2 via STLink
Use the project from the material
6
buf 32
Buffers in Flash, SRAM
HSI*PLL 84MHz
STM32F401RE
Hardware overview
ITM 84MHz
STLink
internal connections
USB
(F4_USART.ioc)
Enable SWO line with debug interface (PB3 pin)
Enable USART2 in asynchronous mode: 115200bps, 8bit data, no parity, 1bit stop
Modify printf() to use SWO or USART2
as an output channels
Configure user button (PC13) to start/stop the print
Configure the transfer complete
callback to send buf[0] using printf
PC13 User button (BLUE)
EXTI13
Irq
Start/Stop
PC
USART2
115200/8/1/no

## Slide 119: Adding SWO, EXTI13 and USART2
STM32CubeMX – Pinout tab
Open F4_USART.ioc project in STM32CubeMX
  Menu File  Open Project
In STM32CubeMX, pinout tab enable SWO pin
  Select SYS  Debug  Trace Asynchronous Sw
Click left button on mouse over PC13 pin and select GPIO_EXTI13 mode
Select USART2 in asynchronous mode
  Select USART2->Mode: Asynchronous
7

## Slide 120: Configure USART2 and EXTI13
STM32CubeMX – Configuration tab
Configure USART2 parameters:
115200 bps / 8 bit data / 1 bit stop / no parity / no HW control
8
Enable EXTI line[15:10] within NVIC configuration

## Slide 121
Generate the code with added new features
Perform further processing in SW4STM32 (F4_USART project)
9

## Slide 122
Using SWO for printf in gcc
In main.c source file:
include the stdio.h library to make printf working
define _write() function used to send data
over SWO using ITM_SendChar() function
as ITM_SendChar() function is accepting single character, we should send data character by character in the loop.
add some messages at the beginning of the application
compile and run the code
10
/* USER CODE BEGIN Includes */
/* USER CODE END Includes */
/* USER CODE BEGIN 4 */
int _write(int file, char *ptr, int len)
{
int DataIdx;
for(DataIdx=0; DataIdx<len; DataIdx++)
{
ITM_SendChar(*ptr++);
}
return len;
/* USER CODE END 4 */
printf("Application start.\n");
/* USER CODE END 2 */
#include <stdio.h>
}

## Slide 123
Using USART2 for printf in gcc
In main.c source file:
include the stdio.h library to make
printf working
define _write() function used to send data over USART2
add some messages at the beginning of the application
int _write(int file, char *ptr, int len)
{
HAL_UART_Transmit(&huart2,(uint8_t*)ptr,len,10);
return len;
}
/* USER CODE BEGIN 2 */
printf("Application start.\n");
printf("Press User button to start new stream\n");
/* USER CODE BEGIN Includes */
#include <stdio.h>

## Slide 124
Sending data over printf
12
In main.c source file (inside USER CODE section) implement own EXTI13 and ADC conversion complete callbacks:
  First one to control start/stop stream
  Second one for sending buf[] using printf() once streaming is stopped
volatile uint8_t flag=1;
const uint16_t buf[32] = {
2047, 2447, 2831, 3185, 3498, 3750, 3939, 4056, 4095, 4056,
3939, 3750, 3495, 3185, 2831, 2447, 2047, 1647, 1263, 909,
599, 344, 155, 38, 0, 38, 155, 344, 599, 909, 1263, 1647};
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
printf("Application start.\n");
printf("Press User button to start new stream\n");
/* USER CODE BEGIN WHILE */
while (1)
{
if(flag) {
for(i = 0; i < 32;i++) {
printf("%d\n",buf[i]);
}
printf("Finished stream\n");
flag = 0;
}
/* USER CODE END WHILE */
void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin){
if(GPIO_PIN_13==GPIO_Pin) {
if(!flag){
printf("Stream stopped\n");
printf("Press button to START a new one\n");
flag=1;
}
else{
printf("Stream started\n");
printf("Press button to STOP it\n");
flag=0;
}
}
}

## Slide 125
13
Analize the data from buf
data sent over USART2
Open serial terminal selecting COM port assigned to Virtual COMP Port (VCP) implemented in STLink, using the configuration:
  115200pbs / 8 data bits / 1 STOP bit / NO parity / NO HW flow control
Reset the board, now you should see “Application start”
message in terminal window
Using copy&paste mechanism copy data to clipboard and then paste them into the spread sheet application (i.e. Excel)
Display the waveform
Chart: 
 | 2047 | 2447 | 2831 | 3185 | 3498 | 3750 | 3939 | 4056 | 4095 | 4056 | 3939 | 3750 | 3495 | 3185 | 2831 | 2447 | 2047 | 1647 | 1263 | 909 | 599 | 344 | 155 | 38 | 0 | 38 | 155 | 344 | 599 | 909 | 1263 | 1647

## Slide 126
14
Change the _write fuction back to the ITM feature
Open STLink Utility
Connect to the board (Target  Connect)
Open SWO viewer window (ST-LINK  Printf via SWO viewer)
Update System clock to 84 000 000 and Stimulus to 0 (toolchain settings)
Start data catching  Start button
Hint: in case there is nothing in trace window, please check the version of STLink firmware -> see the next slide
Analize the data from buf
data sent over SWO

## Slide 127: SWO viewer in STLink Utility
15
In case there is no data in trace window, it is highly probable that
the STLink software on Nucleo board is not up-to-date
To update this software, please follow the below procedure:
  Select ST-LINK->Firmware update
  Press Device Connect button on “ST-Link Upgrade”
window
  After a while there will be information about firmware version on STLink and the current one
  In case the current one has higher number, please upgrade STLink by pressing Yes >>>> button
  After completion of the operation message window will appear
  We can close “ST-Link Upgrade” window and continue
operations on upgraded board.
No data in trace window – upgrade of the driver

## Slide 128
After debugging
preparation for production

## Slide 129: Applications for programming
STVP and STLink-Utility
There are 2 main applications dedicated to programming the STM8 and STM32 devices apart of
the development toolchain:
  STVP – ST Visual Programmer - dedicated for STM8 and STM32 devices
  STM32 STLink Utility – dedicated for STM32 devices
Both come in GUI and command line versions allowing work in semi-automatic mode (serial
programming). Command line versions can be found in the installation folders:
  STLink Utility: c:\Program Files (x86)\STMicroelectronics\STM32 ST-LINK Utility\ST-LINK Utility\ST-LINK_CLI.exe
  STVP: c:\Program Files (x86)\STMicroelectronics\st_toolset\stvp\STVP_CmdLine.exe
Both of them allow programming of all embedded FLASH memory regions
STLink Utility can program external memories (using external software drivers) and monitor SWO input channel (Single Wire Output), a non-intrusive method to monitor activity of the application
Both applications fully support ST-Link programmers (all versions).
10

## Slide 130
STM32 ODE and tools

## Slide 131: STM32 Open Development Environment Building block approach
Move / actuate
Connect
Power
Sense
Process
Software
DATA COLLECT
DATA TRANSMIT
DATA ACCESS
DATA CREATE
DATA POWER
DATA PROCESS
Translate
The building blocks
Your need
Our answer
www.st.com/stm32ode

## Slide 132
STM32 ODE
STM32 X-Nucleo Portfolio
Part Number | Marketing Status | Core Product | General Description
P-NUCLEO-6180X1 | Active | VL6180X | VL6180X Nucleo pack - NEW - Includes VL6180X Expansion board and STM32F401RE Nucleo
P-NUCLEO-6180X2 | Active | VL6180X | VL6180X Nucleo pack - NEW - Includes VL6180X Expansion board and STM32L053R8 Nucleo
X-NUCLEO-6180XA1 | Active | VL6180X | Proximity and ambient light sensor expansion board based on VL6180X for STM32 Nucleo
X-NUCLEO-CCA02M1 | Active | MP34DT01-M | Digital MEMS microphones expansion board based on MP34DT01-M for STM32 Nucleo
X-NUCLEO-IKS01A1 | Active | LSM6DS0; LIS3MDL; LPS25HB; HTS221 | Motion MEMS and environmental sensor expansion board for STM32 Nucleo
Sensors Expansion Boards
Proximity
Motion MEMS
Environmental Sensors
MEMS Microphones

## Slide 133
STM32 ODE
STM32 X-Nucleo Portfolio
Connectivity Expansion Boards
Bluetooth Smart
SubGhz
NFC
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-IDB04A1 | Active | BlueNRG; BALF-NRG-01D3 | Bluetooth low energy expansion board based on BlueNRG for STM32 Nucleo
X-NUCLEO-IDB05A1 | Evaluation | SPBTLE-RF;BlueNRG-MS;BALF-NRG-01D3 | Bluetooth Low Energy expansion board based on SPBTLE-RF module for STM32 Nucleo
X-NUCLEO-IDS01A4 | Active | SPSGRF-868 | Sub-1 GHz RF expansion board based on the SPSGRF-868 module for STM32 Nucleo
X-NUCLEO-IDS01A5 | Active | SPSGRF-915 | Sub-1 GHz RF expansion board based on the SPSGRF-915 module for STM32 Nucleo
X-NUCLEO-NFC01A1 | Active | M24SR64-YMN6T/2 | Dynamic NFC tag expansion board based on M24SR for STM32 Nucleo

## Slide 134
STM32 ODE -
STM32 X-Nucleo Portfolio
Motor Control Expansion Boards
Stepper Motors
Brush DC
NFC
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-IHM01A1 | Active | L6474PD | Stepper motor driver expansion board based on L6474 for STM32 Nucleo
X-NUCLEO-IHM03A1 | Active | powerSTEP01 | High power stepper motor driver expansion board based on powerSTEP01 for STM32 Nucleo
X-NUCLEO-IHM04A1 | Active | L6206 | Dual brush DC motor driver expansion board based on L6206 for STM32 Nucleo
X-NUCLEO-IHM05A1 | Active | L6208 | Bipolar stepper motor driver expansion board based on L6208 for STM32 Nucleo
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-PLC01A1 | Active | CLT01-38SQ7;VNI8200XP | Industrial input/output expansion board based on VNI8200XP and CLT01-38SQ7 for STM32 Nucleo
Input-Output Expansion Boards

## Slide 135: Going beyond with STM32 Open Development Environment
Sense
Motion &
environmental sensors
Proximity sensor
Microphone
Connect
BLE
Wi-Fi
Sub-GHz
NFC
Power
Drive
Power management
LED Boost
Move Actuate
Motor drive
Actuator
Translate
Audio
OpAmp

## Slide 136: Development Tools Function Packs and Open.Software
Jump start design with:
  STM32
  Motion MEMS
  Environmental Sensors
  Microphones
  Connectivity (BLE, SubGHz, WiFi)
Open Software
free SW licensing program
www.st.com/opensoftware
Function Packs
Function Example Projects
www.st.com/stm32ode-fp
Out of the box toolchains compatibility:
  IAR EWARM
  Keil MDK
  AC6 (Eclipse based IDE, GCC based compiler)
OpenSoftware.X libraries
Notes: The Open Software Expansion development suite offers drivers, middleware and application software to jump start your STM32 design with ST products including MEMS motion sensors, Bluetooth smart ICs, environmental sensors, and MEMS microphones. It enables fast prototyping using the STM32 Open Development Environment with leading-edge components that can quickly be transformed into final designs.
The Open Software Expansion environment is made up of several free libraries:
• Open.MEMS: sensor processing libraries for supporting hardware and software architectures including those based on ST’s 6- and 9-axis fusion engines
• Open.RF: protocols and profiles for the wireless connectivity, including the BlueNRG (Bluetooth low energy) library with a comprehensive suite of BT Smart profiles
• Open.Audio: libraries and processing algorithms for audio capturing systems based on digital MEMS microphones (including BlueVoice, a Voice over Bluetooth Low Energy vendor-specific profile)
It also includes implementation examples in the Open.Framework section. The BlueMicrosystem expansion software package uses a Bluetooth low energy (BlueNRG) network processor for communication and includes complete middleware to build applications using pressure, temperature and humidity sensors as well as motion sensors (MEMS). Bluetooth low energy is also used as a communication protocol in the BlueVoiceLink framework, where speech captured by ST digital MEMS microphones is streamed in real-time with very low-power consumption by means of the BlueNRG network processor.
Start your design today with our Open Software Expansion development suite.

## Slide 137: IoT Solutions
Smart
Industry
Smart
Home
Smart
Things
Smart
City
(www.st.com/opensoftware ) | General Description |  |  |  | 
OSXBLUEVOICE | Voice-over-Bluetooth Low Energy vendor-specific profile library for STM32 and BlueNRG |  |  |  | 
osxAcousticBF | Real-time Audio beam forming software expansion for STM32Cube |  |  |  | 
osxAcousticEC | Real-time Acoustic echo cancellation software expansion for STM32Cube |  |  |  | 
osxAcousticSL | Real-time Sound source localization software expansion for STM32Cube |  |  |  | 
OpenSoftware
Open.Audio Libraries
osxMotionAR | Real-time Activity Recognition software expansion for STM32Cube |  |  |  | 
osxMotionCP | Real-time carrying position software expansion for STM32Cube |  |  |  | 
osxMotionFX | Real-time motion-sensor data fusion software expansion for STM32Cube |  |  |  | 
osxMotionGR | Real-time gesture recognition software expansion for STM32Cube |  |  |  | 
OSXSmartConnPS | Bluetooth low energy profiles for the X-CUBE-BLE1 expansion for STM32Cube |  |  |  | 
osxContiki6LP | Contiki OS/6LoWPAN middleware add-on for X-CUBE-SUBG1 expansion for STM32Cube |  |  |  | 
Open.MEMS Libraries
Open.RF Libraries

## Slide 138: IoT Solutions
Smart
Industry
Smart
Home
Smart
Things
Smart
City
(www.st.com/stm32ode-fp) | General Description |  |  |  | 
FP-CLD-BLUEMIX1 | IBM Bluemix Cloud with Wi-Fi, NFC and sensors |  |  |  | 
FP-CLD-AZURE1 | Microsoft Azure Cloud with Wi-Fi, NFC and sensors |  |  |  | 
FP-NET-BLESTAR1 | BLE star network connected via Wi-Fi to IBM Bluemix cloud |  |  |  | 
FP-SEC-BLENFC1 | BLE Secure Pairing: Bluetooth Low Energy and Dynamic NFC tag software expansion for STM32Cube |  |  |  | 
FP-SEC-WIFINFC1 | Wi-Fi Secure Pairing: Wi-Fi and dynamic NFC software expansion for STM32Cube |  |  |  | 
FP-SNS-MOTENV1 | BLE Motion and Environmental sensor node: Bluetooth Low Energy and sensors software expansion for STM32Cube |  |  |  | 
FP-SNS-ALLMEMS1 | BLE Motion, Environmental and microphone sensor node: STM32 ODE function pack for Bluetooth low energy and sensor software expansion for STM32Cube |  |  |  | 
FP-SNS-FLIGHT1 | BLE Motion, Environmental and proximity sensor node: Bluetooth Low Energy, sensors and NFC tag software expansion for STM32Cube |  |  |  | 
Function Packs

## Slide 139: Enabling New Applications
Thermostats and Heaters
Smart Coffee Machine
Smart Microwave
Smart Ovens
Smart Fridges
Smart Washing Machine
Smart DishWasher
Smart AC
Remote Control
Control through BTLE and Wi-Fi
Control through BTLE and Wi-Fi
Control through BTLE and Wi-Fi
Door Motion Sensing
Control through BTLE and Wi-Fi
Refil Order
Programable usage
Water Level and vibration monitoring
Status Alert - Connectivity
Water Level and vibration monitoring
Status Alert - Connectivity
Status Alert – Connectivity
Recipe/Control/Alert through Smart Phone
Humidity and temperature control
Control through BTLE and Wi-Fi
Control through BTLE and Wi-Fi

## Slide 140
Connect

## Slide 141: Connectivity - BlueNRG Expansion Board:
X-NUCLEO-IDB04A1
X-NUCLEO-IDB05A1
Features
  Ultra-low-power Bluetooth low-energy connectivity
  Self-consistent RF design (includes antenna, balun filter, etc.) or module for quicker desing
  SPI communication interface with host MCU
  OUT-OF-THE-BOX:
    Ready-to-use shield-plugin for RF BLE connectivity
    Application examples, quick starting guide and tutorials
  SOFTWARE DEVELOPMENT KIT :
    Extensive examples (source-code and application notes) and API documentation
    Support both ACI and HCI control interfaces over SPI
  Growing library of BLE profiles
  BENEFITS:
    Fast prototyping of user applications, start hands-on coding in 1-day
    No deep Bluetooth low energy connectivity or RF skills required

## Slide 142: Connectivity - NFC Expansion Board:
  The device is a dynamic NFC/RFID tag IC with a dual interface.
  It embeds a 64 Kbit EEPROM memory.
  It can be operated from an I2C interface or by a 13.56 MHz RFID reader or a NFC phone
  NFC antenna: 31 mm x 30 mm 13.56 MHz double layer inductive antenna etched on the PCB (ANT14)
X-NUCLEO-NFC01A1
Features

## Slide 143: Connectivity – SPIRIT Expansion Board:
X-NUCLEO-IDS01Ax
Features
  The X-NUCLEO-IDS01A4, X-NUCLEO-IDS01A5 are evaluation boards based on the SPIRIT1 RF modules SPSGRF-868 and SPSGRF-915
  The SPIRIT1 module communicates with the STM32 Nucleo board host microcontroller through an SPI link available on the Arduino UNO R3 connector.
  SPSGRF SPIRIT1 (Low data-rate, low-power sub-1GHz transceiver) module
  M95640-RMC6TG 64Kbit serial SPI bus EEPROM 64-Kbit serial SPI bus EEPROM

## Slide 144: Connectivity – Wifi Board
X-NUCLEO-IDW01M1 hosts FCC, IC and CE certified SPWF01SA module (FCC ID: VRA-SG9011203, IC: 7420A-SG9011203 and ETSI compliant)
SPWF01SA module major characteristics
compatible with STM32 Nucleo boards
equipped both with ST-morpho and Arduino UNO-R3 connectors
scalable solution; it can cascade multiple boards for larger systems
free development firmware library and examples, compatible with STM32Cube
RoHS compliant
SPWF01SA: low-power Wi-Fi b/g/n SoC with integrated power amplifier and power management and a SMD antenna
X-NUCLEO-IDW01M1
Features

## Slide 145: Example: X-CUBE-MEMS1, Data Logger GUI, Precompiled BIN

## Slide 146: Sensor Board – X-NUCLEO-IKS01A1
DIL24 support for new devices
i.e. LSM6DS3
LIS3MDL
LSM6DS0
LPS25H
HTS221
Motion MEMS sensors
Environmental sensors
www.st.com/mems

## Slide 147: X-CUBE-MEMS1 in 7 steps Use of Sensors_DataLog GUI with precompiled BIN fmw
Download & unpack
www.st.com/X-NUCLEO
www.st.com
1
2
3
4
X-CUBE-MEMS1
X-NUCLEO-IKS01A1
Select
Docs
Sensors Low Level drivers
USB Lib, AST serial
L0 / F4 GUI fmw src code + binary
PC GUI (Sensors_DataLog)
X-CUBE-MEMS1 package structure
Download & install STM32
Nucleo ST-LINK/V2-1 USB driver
stsw-link008
(Link)
5
Download / Install / Run
ST-Link FMW Upgrade Utility
stsw-link007
(Link)
X-CUBE-MEMS1 v2.1
  NUCLEO-F401RE

## Slide 148: X-CUBE-MEMS1 in 7 steps Use Sensors_DataLog GUI with precompiled BIN fmw
drag and drop
DataLog.bin
on Nucleo drive
Open Utilities Folder in the X-CUBE-MEMS1 SW package
7
…and Run Sensors_DataLog
PC GUI
6
\STM32CubeExpansion_MEMS1_V2.1.0\Projects\Multi\Examples\DataLog\Binary\STM32F401RE-Nucleo\
X-CUBE-MEMS1 v2.1
  NUCLEO-F401RE

## Slide 149: X-CUBE-MEMS1 Utilities - Sensors_DataLog
Sensors_DataLog PC GUI
1
Select COM port
3
Select Sensors
2
Select Sensors reading
interval
4
Select Graph Plots
Data Log Area
5
Start Data Logging
X-CUBE-MEMS1 v2.1
  NUCLEO-F401RE

## Slide 150: X-CUBE-MEMS1 Using serial line monitor – e.g.TeraTerm
Close the Sensors_DataLog GUI
Configure the serial line monitor (speed, LF)
Press the BLUE User button on STM32Nucleo
X-CUBE-MEMS1 v2.1
  NUCLEO-F401RE
* IAR project of course also works with the original Binary file

## Slide 151: Example: X-CUBE-BLE1 – uses only the BLE board, for a full example with the Sensor board, use the BlueMicrosystem1_V3.1.1

## Slide 152
Bluetooth Low Energy expansion board
Start coding in just a few minutes with X-CUBE-BLE1
9
Download and unpack X-CUBE-BLE1
Go to www.st.com/x-nucleo
Open project example SensorDemo
1
2
3
4
Download and install STM32 Nucleo ST-LINK/V2-1 USB driver
5
Select
X-NUCLEO-IDB05A1
6
Modify and build application
X-CUBE-BLE1 package
Generic Nucleo docs & BLE porting
BlueNRG SPI driver Bluetooth LE HCI stack
Application examples

## Slide 153: Bluetooth Low Energy expansion board Evaluate using X-CUBE-BLE1 (1/2)
10
1
From X-CUBE-BLE1
software resource package
Drag and drop
SensorDemo.bin on Nucleo drive
2 Download and install the ST BlueNRG application on your smarpthone from Google Play or App Store

## Slide 154: Bluetooth Low Energy expansion board Evaluate using X-CUBE-BLE1 (2/2)
11
Connect your smartphone application to the BlueNRG device and control the cube on the smartphone app
3
Press the user button on the STM32 Nucleo board to rotate the cube on the smartphone app
4

## Slide 155: Example: FP-CLD-bluemix1_software, Post metering data into the IBM Bluemix CLOUD

## Slide 156: Prototyping – IBM Cloud demo
Telemetry, data visualization, alerts, rules etc.
X-Nucleo-IKS01A1
X-NUCLEO-IDW01M1
Nucleo F401RE
MQTT library running on Nucleo + TLS
Nucleo + Wi-Fi + Sensor board+ NFC
Cube based
+ NFC for automatic opening of web page for data visualization
X-NUCLEO-NFC01A1
Vertical application to transmit sensors data to a cloud service base on IBM Bluemix.
FP-CLD-BLUEMIX1
FULL SOURCE CODE AVAILABLE

## Slide 157: IBM Cloud vertical – How To 1/3
Search for FP-CLD-BLUEMIX1 on ST website and get the SW package
Flash Nucleo F401 with binary available in SW package
Connect Wi-Fi, Sensor and NFC expansion boards on top of NucleoF401
1
2
drag and drop
IBMquickstart.bin
on Nucleo drive
3

## Slide 158: IBM Cloud vertical – How To 2/3
Open Hyper terminal, configure it and connect to Nucleo F401
Press RESET button on STM32F401
4
Open Hyper terminal or TeraTerm
Select right COM port
Terminal setup
Serial port setup
5

## Slide 159: IBM Cloud vertical – How To 3/3
6
7
Enter SSID, password and encryption mode of your Access Point (AP)
Demo will connect your AP and start pushing sensors data on the cloud
Visualize sensors data on the web
Open web browser and copy/paste URL provided in hyper terminal e.g. quickstart.internetofthings.ibmcloud.com/#/device/0080E1B4D23F/sensor/ Or Use any NFC enabled tablet/mobile It will automatically open the web browser

## Slide 160: IBM Cloud vertical – View
The ST demo uses the IBM QuickStart visualization website to plot the sensor data vs. time with auto-scaling of the y-axis to the range of data. (The software is unaware of the units of the values.)
ST has on-going programs with IBM Cloud hosting/computing services, Microsoft Azure, and Amazon Web Services (AWS) to start.
https://quickstart.internetofthings.ibmcloud.com/#/device/0080E1B4FA41/sensor/
MAC Address = 0080E1B4FA41
Parameter = A-Temperature

## Slide 161: And just to remember

## Slide 162: ST is a one stop supplier for IOT and other apps
MCU
Signal
transducers
Audio amplifiers
Current sensing
Battery management & monitoring ICs
Bluetooth
SMART
Power management
User interface
Analog front-end
Connectivity
Analog sensors
Digital sensors
Microcontroller
Switches
MEMS microphones
Motion and environmental MEMS sensors
Power management ICs
32-bit
MCUs
ESD Protections
EMI Filters &
RF-IPD
Display Power Supplies and Drivers
NFC & RFID
Smart reset
Protections
Wi-Fi
Modules
Sub 1 GHz

## Slide 163: Which include tons of RF interfaces and all have lib to be handle with our STM32 ;)
NFC family
Wi-Fi Modules
BlueNRG family
www.st.com/brwireless
Bluetooth Modules
Spirit family
SubGHz Modules
Low Power RF
ICs
Low Power RF modules

## Slide 164: Thank you
Bruno.montanari@st.com